## Slide 1
AI FIREGUARD | URIS P0053535 | WORK PROGRAMME TAG3
Yuan Haoming, DSAI | Chief Supervisor: Tsang Yuen Hong
Leakage-Safe Fire & Smoke Detection with YOLOv5
A clean evaluation split exposed a failing legacy checkpoint - retraining recovered independent-test mAP@0.5 from 0.084 to 0.755.
Why this project matters
Discarded cigarettes, smouldering material and delayed smoke recognition can turn small ignition events into major incidents. AI Fireguard investigates camera-based detection that can support earlier alerts and later connect to evacuation planning.
Detection targets: CIGARETTE / FLAME / SMOKE
The audit changed the conclusion
1,511 / 188 / 188
train validation independent test
1,887 cleaned image-label pairs; backgrounds retained as negative samples.
0 source-name, exact SHA-256 or perceptual-hash overlaps across splits.
Class 1 corrected from face-cigarette-smoking to flame.
Raw export
Source groups
Deduplicate
Clean split
Reproducible local training
YOLOv5s | 45 epochs | 640 x 640
Batch 8 | Apple MPS | 2 workers | seed 0
Initialization: legacy best.pt; all layers unfrozen
2 h 04 min training | 0 swaps | 14 MB model
A fair test exposed the legacy gap
The legacy run looked strong on its own validation artifact, but the same checkpoint collapsed on the non-overlapping clean test. The drop is diagnostic evidence of evaluation leakage and label mismatch - not a model regression.
Chart: mAP comparison across evaluation states
| Legacy val* | Legacy clean | Retrained clean
mAP@0.5 | 0.889 | 0.084 | 0.755
mAP@0.5:0.95 | 0.582 | 0.033 | 0.453
*Legacy validation is not directly comparable: old split and old class definition.
0.755
independent test mAP@0.5
0.453
independent test mAP@0.5:0.95
Retraining recovered 85% of the legacy artifact's mAP@0.5 while using a genuinely independent test split.
Independent test summary
Precision 0.841 Recall 0.680
188 images | 171 objects | 11.3 ms/image at batch 8
Performance is strongest on smoke
Chart: Average precision by class
| Cigarette | Flame | Smoke
AP@0.5 | 0.717 | 0.763 | 0.786
AP@0.5:0.95 | 0.404 | 0.36 | 0.595
Class Precision Recall Instances
Cigarette 0.794 0.634 82
Flame 0.812 0.740 50
Smoke 0.919 0.667 39
Training remained stable
Losses declined while recall and both mAP measures continued to rise through the final epochs.
Qualitative evidence
Left: single-image flame detection (0.31). Right: normalized clean-test confusion matrix.
What the errors mean
Smoke leads: precision 0.919 and AP@0.5:0.95 0.595.
Cigarette recall remains 0.634: small targets and hand occlusion still matter.
Flame recall is 0.740, but AP@0.5:0.95 is 0.360: localization needs improvement.
Missed targets dominate more than cross-class confusion on the clean test.
Deployment and next steps
Add small-cigarette, low-light, occlusion, fog and steam hard negatives.
Calibrate confidence per class and test temporal consistency on video.
Validate on unseen buildings before safety-critical deployment.
Connect verified alerts to the escape-route planning prototype.
Trustworthy splitting changed the story: the detector now generalizes on a clean test instead of only scoring well on its own validation data.
Sources: URIS progress report; leakage audit; full_clean_45e; independent clean test. Full methods and weights:
github.com/Llleeeo/Smoke-and-Fire-detection-model-and-implementation-
Notes: [Sources]
- docs/Undergraduate Research and Innovation Scheme.pdf (project title, author, supervisor, motivation, original workflow)
- training/leakage_safe_yolov5/EXPERIMENT_RESULTS.md (clean dataset, test metrics, class metrics, resource usage)
- training/leakage_safe_yolov5/audit/verification.json (zero cross-split overlaps)
- training/leakage_safe_yolov5/original_model_reference/results.csv (legacy validation artifact)
- training/leakage_safe_yolov5/runs/full_clean_45e/results.csv and results.png (training trajectory)
- training/leakage_safe_yolov5/runs/full_clean_test/confusion_matrix.png (clean-test confusion matrix)
- training/leakage_safe_yolov5/runs/full_clean_inference/000017_jpg.rf.89254c89fc5700eff8d14d33bc9cc307.jpg (inference example)
- https://github.com/Llleeeo/Smoke-and-Fire-detection-model-and-implementation- (repository)
[/Sources]